## Slide 1
Open-Set Driver Identification
from Heavy-Duty J1939 CAN Data
using Time-Series Foundation Models
Capstone proposal
Atul Prem Patnala · University of North Carolina Wilmington
Building on TruckIDMe, IEEE AIMS 2025 (Vienna)

## Slide 2
Behaviour-based biometrics: a new frontier in driver verification
Who is actually driving this truck — and can we tell without adding hardware?
CONVENTIONAL VERIFICATION
▪ Keys, fobs, PINs — verify once, at login
▪ Face / fingerprint readers: invasive and privacy-sensitive
▪ Require extra hardware in every cab
▪ Vulnerable to spoofing, sharing and theft
▪ Nothing detects a driver swap after the engine starts
BEHAVIOUR-BASED VERIFICATION
▪ Uses signals the truck already broadcasts
▪ Passive — verification *during* driving, not just at login
▪ Privacy-preserving: no camera, no biometric enrolment hardware
▪ Harder to spoof — style is not a credential that can be handed over
▪ Hardware-free → deployable across an existing fleet
Notes: Frame the security need first: fleets need continuous verification, not a one-time check.

## Slide 3
Why J1939 CAN data, and what we are asking
The hidden fingerprint inside every commercial truck
WHY CAN SIGNALS
▪ The bus carries every pedal press, torque request and brake application
▪ Rich internal dynamics: torque demand, engine load, fuel rate, turbo
▪ Fine-grained behavioural signal at native rates (10 ms–1 s)
▪ No extra sensors: no GPS, IMU, camera or phone required
WHY J1939 IS SPECIAL
▪ Standardised PGNs / SPNs across all commercial trucks
▪ Identical signal meaning regardless of manufacturer
▪ Vendor-agnostic → scalable to thousands of vehicles
▪ Supports fleet-wide behavioural modelling, not one-car studies
WHAT WE ASK
▪ Can a truck driver be identified from CAN behaviour alone?
▪ And the harder question: can the system recognise a driver it has never enrolled?
▪ Fleet need: unauthorised swaps, misuse, tampering, theft
▪ Closed-set answers the first. Open-set answers the second.
Notes: Slide 2 is the motivation; this slide narrows to the research question. The open-set question is the project.

## Slide 4
The dataset: ORNL Driver Identification
Collected by Colorado State University for Oak Ridge National Laboratory
WHAT IT CONTAINS
▪ 50 drivers, 2014 Kenworth T270 (Class 6)
▪ Identical 20-mile / 50-minute route, Fort Collins CO
▪ CAN-bus (J1939), GPS, IMU, heart rate + scripted cyberattack
▪ Three groups: Control 17 · Aware 16 · Aware+Protocol 17
▪ Native sampling rates, plus a 1 Hz downsampled release
WHAT IT MEANS FOR THIS WORK
▪ 46 usable drivers — G1S04 (low CAN rate) and G1S10–12 (clock failure) excluded
▪ The attack hit only the instrument cluster, a separate bus → behaviour signals are truthful
▪ Largest driver pool at native CAN rates in the published literature
▪ ⚠ One drive per driver — identity and trip are confounded
▪ ⚠ One vehicle, one route, one city
Notes: Be explicit about the single-session limitation here; it returns in the evaluation design.

## Slide 5
Prior work: TruckIDMe (IEEE AIMS 2025, Vienna)
Where this project starts — closed-set identification on the same dataset
▪ Pipeline: 1 Hz downsampling → 5 aggregates per signal (min, max, mean, std, median) → sparsity filtering → windowing
▪ Split: driver-wise, chronological, with a one-window gap between train and test to prevent temporal leakage
▪ Selection: Random-Forest importance ranked 262 columns → top 6 features (>90% cumulative importance)
▪ Results: Decision Tree ~94.9% · Random Forest ~0.98 · KNN ~0.994 · MLP ~91.3%; AUC > 0.97
▪ Its own stated future work: modern sequence models, better feature selection, behavioural drift and generalisability
▪ This proposal takes up that future work — and asks the question the paper could not: what about drivers the model has never seen?
Notes: Keep this brief and forward-looking: the prior paper closes on exactly the questions this proposal opens.

## Slide 6
Literature 1/3 — the data the field relies on
Almost everything published rests on decoded OBD-II at 1 Hz or slower, with few drivers — full inventory of all 25 datasets in the backup slides
Dataset | Drivers | Vehicles | Data type | Rate | Route
ORNL (ours) | 46 usable | 1 truck | raw J1939 → SPNs | native (10 ms–1 s) | fixed
CIAIR (2007) | 274 | 1 van | speech + video + sensors | — | naturalistic
KCID (2025) | 16 | 4 | raw CAN | 1,000–2,500 Hz | daily + fixed
Hallac (2016) | 64 | 10 | real-world sensors | — | single turn
HCRL (2016) | 10 | 1 | decoded OBD-II | 1 Hz | fixed
Barreto 19drivers | 19 | 1 | decoded OBD-II | 0.14 Hz | fixed
UK 19 Drivers (2021) | 19 | 1 | decoded OBD-II | 1 Hz | fixed
Notes: Kidmose et al. 2025 make this case: decoded data, low rates, fixed routes, single vehicles, no demographics.

## Slide 7
Literature 2/3 — what has been tried, and what it missed
Four representative studies: strong results, weak evaluation
FOUNDATIONS
▪ Enev 2016 (PoPETs): 15 drivers; the brake pedal alone gives 87% from 15 min, 100% from 1.5 h
▪ Decimation to 60 Hz justified by human actuation bandwidth
▪ Fingerprint survives different roads and days (91%)
▪ Kwak 2017: 51 → 15 features, statistics per 60 s window, threshold-based verification, >99%
DEEP LEARNING
▪ Hu 2023 (IET): CNN + BLSTM ensemble, 20 drivers, 0.96
▪ Augmentation matters most when data is scarce: +15.2 pts at 1 min of training data
▪ Shin 2025: CAN → images → ResNet-18, continuous retraining
▪ Detects an unregistered driver, but with a softmax over 3 drivers
THE COMMON FLAWS
▪ 10–20 drivers at 1 Hz, single vehicle, fixed route
▪ Overlapping windows under random splits — near-duplicates on both sides
▪ No leakage audit: Kwak's top features are transmission oil temperature and fuel trim — values a driver *cannot* control
▪ Same-session evaluation: Shin shows 67–78% within a session vs 33–49% across sessions
Notes: The third card is the argument: published accuracies are inflated by evaluation design, not by better modelling.

## Slide 8
Literature 3/3 — the tools this proposal brings in
Time-series foundation models, cross-domain transfer, and few-shot enrollment
MANTIS (2026)
▪ Foundation model built for time-series classification
▪ 4.2M parameters — fine-tunable on a single GPU
▪ Frozen encoder beats larger models: UCR 0.820 vs MOMENT 0.779
▪ Channel adapters (PCA / linear) for multivariate input
▪ Pre-trained on purely synthetic data
DOES IT TRANSFER? (EEG, 2025)
▪ Fine-tuned Mantis beats EEGNet and CBraMod, an EEG-specific foundation model
▪ "Freezing the encoder leads to a huge decrease" → fine-tuning is necessary
▪ Pre-training gains are modest: +0.3 to +5 points over random init
▪ Compresses 6,000 samples → 512 and still wins
FEW-SHOT ENROLLMENT (P-AttEnc, 2025)
▪ Driver = mean embedding of a few labelled windows (a *prototype*)
▪ New driver enrolled by storing windows — no retraining
▪ This is what makes open-set possible
▪ ⚠ Their unknown-driver result (65.7%) is a 2-way test; chance is 50%
Notes: Mantis is the model, EEG is the transfer evidence, P-AttEnc is the enrollment mechanism.

## Slide 9
Research gap
Five gaps; this proposal addresses the first two directly
▪ 1 — Open-set is rudimentary. Thresholds exist (Kwak 2017, Shin 2025) but none is calibrated, none reports a threshold-free metric, none evaluates at scale
▪ 2 — No foundation models have been applied to CAN driver identification. Evidence exists for UCR/UEA, human activity, EEG and gas sensors — not for vehicle buses
▪ 3 — Leakage is rarely audited. Cumulative counters, fuel level and thermal state separate drivers perfectly for non-behavioural reasons; almost no study screens for it
▪ 4 — Same-session evaluation inflates results. 67–78% within a session vs 33–49% across sessions (Shin 2025)
▪ 5 — Multi-rate CAN is never addressed. J1939 spans 10 ms to 1 s per signal; published datasets arrive pre-aligned at 1 Hz, so the problem is invisible
Notes: Gaps 3-5 are methodological and shape the evaluation; gaps 1-2 are the contribution.

## Slide 10
Hypothesis and research questions
One hypothesis, four questions, each answerable within the term
HYPOTHESIS
▪ Only ~40 minutes of data exist per driver — too little to train a deep model from scratch
▪ A model pre-trained on large time-series corpora should therefore identify drivers more effectively than hand-engineered features
▪ And its embedding space should support rejecting drivers it never enrolled
▪ Open question, not an assumption: no CAN data appears in any pre-training corpus
RESEARCH QUESTIONS
▪ RQ1 — Separability. Do frozen embeddings separate drivers on audited CAN signals?
▪ RQ2 — Expert vs generic prior. Do they beat hand-engineered features under one identical split?
▪ RQ3 — Open-set. Can a calibrated rejection rule separate 10 unenrolled drivers from 36 known ones?
▪ RQ4 — Data efficiency. How does accuracy decay as labelled data per driver shrinks?
Notes: RQ2 is the scientific core: expert prior versus generic temporal prior under scarcity.

## Slide 11
Proposed work 1/3 — pipeline
From raw J1939 to model input, with leakage controlled at the front
▪ Signal integrity first. Keep only audited signals: η² (between-driver variance) plus physical reasoning about what each signal measures. Cumulative counters, fluid levels and the thermal/ambient family are excluded as trip-state proxies
▪ Multi-rate alignment. Fast signals: mean per 100 ms (decimation with a built-in anti-alias filter). Slow signals: zero-order hold — literally CAN semantics
▪ Windowing. Non-overlapping windows; two lengths compared: 51 s (512 steps, the model's native input) and 120 s (resized), where our own accuracy saturates
▪ Representation. Mantis embeddings, intermediate layer, [CLS] + mean-token concatenation; PCA channel adapter if the channel count demands it
▪ Frozen first, fine-tune second — frozen is a cheap measurement; the EEG and e-nose evidence says fine-tuning will be needed
Notes: The audit is the part no prior CAN study does; it is what makes the eventual number believable.

## Slide 12
Proposed work 2/3 — the open-set design
Enrollment by prototype; rejection by distance
ENROLLMENT (no retraining)
▪ Each driver is represented by a prototype: the mean embedding of their earliest windows
▪ A new driver is added by storing windows, not by retraining the model
▪ Query windows are matched to the nearest prototype
▪ Mechanism borrowed from prototypical networks (P-AttEnc)
REJECTION (the open-set part)
▪ A softmax over 36 drivers can never output "unknown" — the probabilities always sum to one
▪ So rejection uses a separate score: distance to the nearest prototype
▪ Threshold calibrated on known drivers only — never on the unknown set
▪ Reported threshold-free as AUROC, so the result does not depend on one cutoff
Notes: This is the methodological contribution: calibrated rejection, not a fourth class.

## Slide 13
Proposed work 3/3 — evaluation
Designed so the numbers survive scrutiny
▪ Driver split: 36 known / 10 unknown, repeated over 5 random partitions stratified by awareness group, reported as mean ± std
▪ Temporal split: within each known driver — train first 70%, discard a 5% gap, test last 25%, so train and test cover different route positions
▪ Metrics: top-1/2/5 among the 36 known (chance 2.8%) · AUROC for known vs unknown · learning curve over enrollment size
▪ Baselines under the identical split: our 9-aggregate Random Forest (50% top-1 from 2 min) and Catch22 features
▪ Central ablation: the same architecture from random init, from the synthetic checkpoint, and from the real-data checkpoint — the gap between them *is* the value of pre-training
Notes: Every prior study we reviewed fails at least one of these; that is the point.

## Slide 14
Expected contributions and risks
What this produces, and what could go wrong
CONTRIBUTIONS
▪ First application of a time-series foundation model to CAN driver identification
▪ Open-set evaluation with a calibrated rejection threshold and AUROC, at 46-driver scale
▪ A leakage-audited benchmark on native-rate J1939 — an honest baseline the field currently lacks
▪ A direct measurement of expert features vs a generic temporal prior under data scarcity
RISKS AND MITIGATIONS
▪ Frozen embeddings may not separate drivers → fine-tuning budgeted from week 5
▪ Trip confound: one drive per driver, so identity and session cannot be fully separated → audited signals + declared as a limitation
▪ Dimensionality: ~62 channels × 512 dims vs ~1,200 windows → PCA adapter, regularised head
▪ Transfer evidence is about signals, not identity — EEG studies split *by subject*; we do the opposite
Notes: Naming the risks up front is stronger than being asked about them.

## Slide 15
Timeline — 10 weeks
22 September → Thanksgiving week (26 November 2026)
Phase | Weeks | Dates | Deliverable
Foundation | 1–2 | 22 Sep – 3 Oct | Audited windowed tensor; environment + Mantis running; frozen embeddings extracted
Separability + baselines | 3–4 | 6 – 17 Oct | RQ1 measured (KNN / nearest-centroid, t-SNE); RF and Catch22 baselines on the identical split
Open-set | 5–6 | 20 – 31 Oct | Prototype enrollment, rejection score, AUROC over 5 partitions (RQ3)
Fine-tuning + efficiency | 7–8 | 3 – 14 Nov | Random vs synthetic vs real ablation (RQ2); learning curve over enrollment size (RQ4)
Analysis + write-up | 9–10 | 17 – 26 Nov | Ablations, error analysis by group, figures, final report and defence slides
Notes: Week 4 is the decision point: if frozen embeddings separate drivers, weeks 7-8 become extensions; if not, they become fine-tuning.

## Slide 16
Backup slides
One slide per reviewed paper — for questions, not for the talk
Notes: Delete from here onward if the deck must be exactly 15 slides.

## Slide 17
1
Lanigan et al. (2025) — the dataset
Journal of Transportation Security · peer-reviewed
THEIR POV
▪ 50 drivers, one 20-mile / 50-minute route, Fort Collins; 2014 Kenworth T270
▪ 3×2 design: awareness (Control / Aware / Aware+Protocol) × experience
▪ Cyberattack mid-route: needles to zero, all warning lights, 2 Hz tone
▪ Instrument cluster only — no control system affected
▪ Awareness alone is not enough: stop rate 9% → 30% → 100%
▪ Reaction time 30.3 s → 16.1 s → 7.5 s with a response protocol
MY POV
▪ SOPs matter: awareness plus explicit instructions
▪ The attack never touches J1939 → our behaviour signals are truthful
▪ One drive per driver → driver and trip are confounded
▪ G3's 100% stop rate may explain why G3 is hardest to classify — the protocol homogenises behaviour
▪ A window overlapping the attack could leak group, not identity
Notes: Our data source, but its research question is human factors, not identification.

## Slide 18
2
Kidmose et al. (2025) — KCID
arXiv preprint · dataset review + new raw-CAN dataset
THEIR POV
▪ Reviews 6 public driver-fingerprinting datasets
▪ Frames driver authentication as anti-theft defence-in-depth
▪ All public sets are decoded OBD-II, mostly ≤ 1 Hz (Barreto: 0.14 Hz)
▪ Raw CAN wins on coverage, temporal resolution, fidelity
▪ Costs: noise and interpretability; Bluetooth adds latency and packet loss
▪ Five gaps: decoded data · low rates · fixed routes · single vehicle · no demographics
MY POV
▪ Justifies our data choice: native rates, more drivers than any set they review
▪ Their "filter the noise" advice is our leakage audit, done more rigorously
▪ Two criticisms land on us: fixed route, single vehicle — declare both
▪ They never say "open-set" and never claim saturation → the framing is ours to argue
▪ ORNL is absent from their review — an under-used resource
Notes: Cite for motivation, not for the open-set framing itself.

## Slide 19
3
Enev et al. (2016) — the foundational result
Proceedings on Privacy Enhancing Technologies · peer-reviewed
THEIR POV
▪ 15 drivers, one 2009 sedan; parking-lot maneuvers + 50-mile open-road loop
▪ Brake pedal alone: 87.3% from ~15 min, 100% from 1.5 hours
▪ All sensors → 100% on open road; accelerator pedal alone only 18–31%
▪ Quadratic interpolation + decimation to 60 Hz, justified by Nyquist
▪ Fingerprint stability: same driver, different roads and days → 91%
MY POV
▪ A single direct-action signal can carry identity → channel choice beats channel count
▪ Free driving beats prescribed maneuvers (50% vs 87–100%)
▪ We improve the order: filter before decimating; they denoise after
▪ Their stability result contradicts Shin's drift finding
▪ They scale using test data — a leak we will not copy
Notes: Everything else in the field builds on this paper.

## Slide 20
4
Kwak et al. (2017) — Know Your Master
arXiv preprint · origin of the HCRL / OCSLab dataset
THEIR POV
▪ 10 drivers, KIA Soul, 23 km in Seoul, 1 Hz OBD-II, two round trips each
▪ 51 features → 15 by InfoGain ranking; min–max scaling
▪ mean / median / std per 60 s window → DT, RF, KNN, MLP
▪ Statistical features are the win: MLP 0.747 → 0.964
▪ Verification by threshold (0.97) → alert the owner
▪ >99% on all road types; parking lot lowest
MY POV
▪ Their top features are transmission oil temperature and long-term fuel trim…
▪ …praised precisely because "the driver cannot manipulate these data"
▪ That is the error we correct: if it can't be manipulated, it isn't behaviour
▪ 60 s windows stepping 1 s + 10-fold CV → near-duplicates across every fold
▪ Thresholded rejection exists since 2017 → our contribution is calibration, AUROC, scale
Notes: The clearest published example of the leakage problem our work addresses.

## Slide 21
5
Hu et al. (2023) — ensemble deep learning
IET Intelligent Transport Systems · peer-reviewed
THEIR POV
▪ M 1-D CNN + BLSTM bagging ensemble; 20 drivers, 8 CAN signals
▪ No attention mechanism
▪ Ensemble 0.9595 vs 0.9475 / 0.9133 — the gain is mostly stability
▪ Parameters: MLP 762k · ResNet 514k · M 1-D CNN 90k · LSTM 6k
▪ Four augmentations: sliding window · noise · reversal · random drift
▪ Test set = last 30% of the drive (chronological)
MY POV
▪ Augmentation pays most when data is scarce: +15.2 pts at 1 min, +1.3 pts at 15 min
▪ Ranked for us: sliding window → drift → noise → reversal
▪ Drift may make the model invariant to slow trip-state offsets
▪ Reversal turns braking into acceleration → do it last
▪ Accuracy doesn't track parameter count → small models are viable
Notes: The scarcity curve is the strongest argument for our data-efficiency framing.

## Slide 22
6
Shin et al. (2025) — MLOps, MTF images, drift
Electronics (MDPI) · peer-reviewed journal
THEIR POV
▪ CAN → Markov Transition Field images → ResNet-18 on Google Cloud
▪ Continuous retraining; only models > 70% validation accuracy deploy
▪ Old-data model 33–49% vs recent-data model 67–78%
▪ Detects unregistered drivers via multi-maneuver voting
▪ Only turns exceed 70% — straight, stop and start fail
MY POV
▪ Images give structure at the cost of precision — and unlock the CNN ecosystem
▪ Their "drift" test is really cross-session vs same-session (~20-month gap)
▪ → the best evidence that our same-session numbers are upper bounds
▪ Unregistered-driver detection already exists → our claim must be sharper
▪ Borrow their visualisation habit: t-SNE by driver, then by trip phase
Notes: Reframe their drift result as session variability; our best citation for the trip confound.

## Slide 23
7
Lee et al. (2025) — P-AttEnc: few-shot prototypes
arXiv preprint
THEIR POV
▪ Driver ID framed as multivariate time-series classification
▪ Attention-only encoder: 87.6% fewer parameters, 44–79% faster
▪ Prototypical network: driver = mean embedding of a few labelled windows
▪ Classified by Euclidean distance to the nearest prototype
▪ Closed-set 99.0–99.9%; 10-way 1-shot 69.8%; "unknown drivers 65.7%"
MY POV
▪ The mechanism transfers: Mantis embeddings → prototype → nearest match
▪ = enrollment without retraining, which is what makes open-set possible
▪ "65.7% on unknown drivers" is a 2-way test — chance is 50%
▪ 10 drivers per dataset; 30 s windows with 50% overlap, random split
▪ No channel selection, no multi-rate handling, no sampling rate stated
Notes: Take the mechanism, not the evaluation.

## Slide 24
8
Feofanov et al. (2026) — Mantis
arXiv preprint · classification-native time-series foundation model
THEIR POV
▪ 4.2M parameters; contrastive pre-training on purely synthetic data
▪ Input resized to 512 steps → 32 tokens
▪ Frozen encoder beats larger models: UCR 0.820 vs MOMENT 0.779
▪ Out-of-distribution sensors: Mantis 0.582 vs MOMENT 0.308
▪ Channel adapters (PCA or linear, d → 10) improved all 10 multivariate sets
▪ Best features come from an intermediate layer, not the last
MY POV
▪ One channel at a time — the encoder never sees two signals together
▪ True zero-shot is impossible for identity: their "zero-shot" still trains a classifier
▪ Open-set rejection needs a separate score — Mantis provides none
▪ Its tokeniser already encodes first-order differences = our "jerkiness" finding
▪ It keeps unnormalised patch mean/std → absolute levels survive → audit still required
Notes: Primary candidate: classification-native, small enough to fine-tune.

## Slide 25
9
Gnassounou et al. (2025) — does it transfer?
arXiv preprint · generic TSFMs applied to EEG · same authors as Mantis
THEIR POV
▪ Fine-tuned Mantis on EEG: motor imagery (109 + 25 subjects), sleep staging (8 datasets)
▪ Beats EEGNet and CBraMod, an EEG-specific foundation model
▪ Wins every sleep dataset (MASS 84.1 vs 81.1 vs 79.9)
▪ Synthetic pre-training matches or beats real-data pre-training
▪ Channel-independent Mantis beats CBraMod's multivariate design
MY POV
▪ "Freezing the encoder leads to a huge decrease" → fine-tuning is necessary
▪ They dropped MOMENT purely because it is too big to fine-tune
▪ Pre-training gains are modest (+0.3 to +5 pts) over random init
▪ ⚠ They split by subject — identity is a nuisance there; for us identity is the label
▪ Adopt their design: random vs synthetic vs real pre-training = our core ablation
Notes: Transfer evidence for the proposal — but it shows Mantis handles unfamiliar signals, not that it separates individuals.

## Slide 26
Backup — public driver-identification datasets
Every public dataset named across the ten reviewed papers
Dataset | Drivers | Vehicles | Data type | Rate | Sessions
ORNL (ours) | 50 → 46 usable | 1 truck | raw J1939 → SPNs | native 10 ms–1 s | 1
CIAIR (Nagoya) | 274 | 1 van | speech + video + sensors | — | multiple
KCID (2025) | 16 | 4 | raw CAN | 1,000–2,500 Hz | multiple
HCRL / OCSLab (2016) | 10 | 1 | decoded OBD-II | 1 Hz | 2 round trips
Barreto dailyRoutes (2018) | 14 | 14 | decoded OBD-II | 0.14 Hz | daily
Barreto 19drivers (2018) | 19 | 1 | decoded OBD-II | 0.14 Hz | fixed route
AEGIS (2019) | 3 | 1 | decoded OBD-II + GPS | 20 Hz | not stated
This Car is Mine! (2019) | 4 | 1 | decoded OBD-II | 1 Hz | fixed route
UK 19 Drivers (2021) | 19 | 1 | decoded OBD-II | 1 Hz | ~32 min/driver
Vehicular data trace | 10 | — | CAN-bus | not stated | 36 journeys
hciLab driving | 10 | — | GPS + accelerometer | not stated | 0.5 h total
Notes: Only KCID and ORNL avoid decoded OBD-II. Only ORNL has a single session per driver.

## Slide 27
Backup — private and simulator datasets in the literature
Cited inside the reviewed papers; originals not read (secondary sources)
Study | Drivers | Data | Reported result | Type
Hallac et al. (2016) | 64 | real-world sensors, 10 vehicles | 76.9% (2 drivers) → 50.1% (5) | private
Lestyán et al. | 33 | raw CAN, 8 vehicles | RF re-identification | private
Dong et al. (ARNet) | 50 | GPS | 40.4% top-1 / 78.3% top-5 | private
Enev et al. (2016) | 15 (+1) | stock sensors, 60 Hz | 100%; stability 91% across days | private
Rahim et al. | 25 | CAN events | 95.89% (RF) | private
Sánchez et al. | 25 | acceleration → 2-D | 71.89% top-1 | private
Jeong / Xun et al. | 20 | CAN | CNN | private
Hu et al. own (2023) | 20 | 8 CAN signals | 0.96 (ensemble) | private
Choi et al. | 9 | CAN | 31.45% (HMM) | private
Shin et al. own (2025) | 3 + 1 intruder | ~300 CAN columns, 1 Hz | 67–78% same-session | private
Wakita et al. | 30 | simulator, guide vehicle | 73% | SIMULATOR
Zhang et al. | 20 | simulator, multi-day sessions | 85% (HMM) | SIMULATOR
Lee et al. (2022) | 7 | simulator | +19.94% over CNN | SIMULATOR
Notes: Flag the simulator rows when comparing: participants reported the simulator imitated braking poorly (Enev).